## Slide 1: ECSE 436: Lempel-Ziv COMPRESSION ALGORITHMS for INFROMATION SOURCES
AUTHORS:
CHROUK KASEM: 260 512 917
MUHAMMAD TAHA: 260 505 597
PROJECT SUPEVISOR: PROFESSOR JAN BAJCSY

## Slide 2: Overview
Introduction
  Background
  Project Objectives
Lempel-Ziv Compression Algorithm
  Theory
  Extension
Implementation and Results
  Implementation
  Results

## Slide 3: 1. Introduction: Background
Compression:
- Saves Bandwidth - Saves disk storage space
- Lowers transmission time -Improves transmission efficiency
In 2011, EMC cloud computing company estimated that the data in the world is:
1.8 Zettabytes 1.8 × 10 21
A survey in 2014 concluded that every minute, 72 hours of video content is uploaded on YouTube and Google receives over 4 million search queries.

## Slide 4: 1. Introduction: Background
The modern data compression is based on Claude Shannon’s paper “A Mathematical Theory of Communication” published in 1948. [1]
Huffman | Run-Length | Lempel-Ziv | Turbo Compression
JPEG | Black and white scans | GIF | 3G/4G mobile communications
MP3 | Fax Machines | ZIP | Satellite Communications
Claude Elwood Shannon (1916–2001) [4]
Applications of compression codes [5]
Shannon source coding theorem: H(X) ≤ E(L)
Kraft’s inequality must be satisfied by any Uniquely Decodable Code:
Equation

## Slide 5: 1. Introduction: Project Objectives
Main Objective: Implement, evaluate and test Lempel-Ziv data compression algorithm
Identified the following algorithms for designing:
Adaptive fixed window with fixed length match encoder and decoder
Adaptive sliding window with fixed length match encoder and decoder
Adaptive sliding window with variable length match encoder and decoder
Simulations with different
  sizes of windows/matches
  input sizes
  Sources: i.i.d. and Markov Sources

## Slide 6: 2.1 Lempel-Ziv Algorithm
0 0 0 1 0 1 1 0 1 0 1 1 1 0 1 1 0 0 0 1 0 1 1 0 0 1 0 1 1 0 1 1 1
H(X) =P0× + (1- P0)×
Window size given by: W = n2 2nH(X)
An example of adaptive Lempel-Ziv compression with n = 3, P0 = 0.6 and P1 = 0.4, assuming window size of 211:
Flag = 1 Pointer = 5 (01001)
1. The window size using the formula W = n2 2nH(X) with P0 = 0.6 and P1 = 0.4 gives W = 70; it’s not used in the example for illustrative reasons.
Flag = 1 Pointer = 1 (00001)
Encoded output = 1 0 1 0 0 1 1 0 0 0 1 1 0 0 0 1 1 0 1 1 1

## Slide 7: 2.2 Lempel-Ziv Algorithm Extension
Find matches beyond or below size of match(n):
  Captures evolving source statistics
Sliding window implementation extended from version 3 implementation
0 0 0 1 0 1 1 0 1 0 1 1 1 0 1 1 0 0 0 1 0 1 1 0 0 1 0 1 1 0 1 1 1
length = 3
length = 2
Encode codeword to : [Flag, Pointer, Length]

## Slide 8: 3. Implementation and Test Results
LZ Encoder
LZ Decoder
Error Free Channel
Input Data
Decompressed lossless data

## Slide 9: Testing Results
Running simulations for i.i.d source with P0 = 0.90 for different matches of n = 2, 5, 10, 20, 25, 50, 80, 100 with input file size 104
Observation: Although the probability of matches is high for n= 2, 5, 10, the pointer is larger than the original symbol size
9

## Slide 10: Testing Results
Running simulations for i.i.d source with P0 = 0.95 for different matches of n = 2, 5, 10, 20, 25, 50, 80, 100 with input file size 104
Observation: This i.i.d source performs better than the last one with probability of 0 of 0.90
10

## Slide 11: Testing Results
Running simulations for Markov source with P0 = 0.95 for different matches of n = 2, 5, 10, 20, 25, 50, 80, 100 with input file size 104
Observation: Markov sources aren’t compressed using Lempel-Ziv although there is a very large probability of match, which generally implies that source should ideally compress to entropy H(X) for an infinitely large n
11

## Slide 12: 3. Conclusion
Learnt and implemented adaptive Lempel-Ziv compression
Learnt design and implementation of signal processing functions in MATLAB
The size of the pointer plays a huge role in compression; optimal size of match(n) was found to be around 25 for large source files.
Further implementation includes done into extending this algorithm to variable length matches.

## Slide 13: 5. References
[1] S. W. 2002, "Historical notes: History [of data compression]," 2002. [Online]. Available: https://www.wolframscience.com/reference/notes/1069b.
[2] R. T. Snodgrass, Radio Receiving for Beginners, V. F. Camp, Ed. New York: The MacMillan Company, 1992.
[3] A-Read, "Satellite communication systems," in A Read. [Online]. Available: http://www.a-read.com/satellite-communication-systems/.
[4] Bell Labs, "Claude Elwood Shannon 1916-2001," in wikipedia.com, 2011. [Online]. Available: http://it-science.net/images/shannon.small.jpg.
[5] J. G. Proakis, Communication Systems Engineering, M. Salehi, Ed., 2nd ed. Pearson, 2001.
Thank You!

## Slide 14: Backup Slides

## Slide 15: Software Used
Used MATLAB to code these functions.
Reason for choosing MATLAB:
  It’s extensive Math Library.
  Easy to deal with vectors and matrices
Implementation on other programming languages, for example C or JAVA, will be very simple after coding on MATLAB.

## Slide 16: Source Encoder/Decoder

## Slide 17: Channel Encoder/Decoder

## Slide 18: Universal Communication Systems Architecture

## Slide 19: Huffman Encoding: Practical Example

## Slide 20: Semester’s Timeline