## Slide 1: Lempel-Ziv COMPRESSION ALGORITHMS for INFROMATION SOURCES
AUTHORS:
CHROUK KASEM- ECSE 456: 260 512 917
MUHAMMAD TAHA-ECSE 456: 260 505 597
PROJECT SUPEVISOR: PROFESSOR JAN BAJCSY

## Slide 2: Overview
Introduction
  Background
  Motivation and Challenges
  Project Description
Lempel-Ziv Compression Algorithm
  Theory
  Implementation
Implementation and Results
  Implementation
  Results

## Slide 3: 1. Introduction: Background
Early compression in the 1800’s (Morse code). [1]
Key idea: Frequent symbols LESS BITS
Example of Morse code [2]

## Slide 4: 1. Introduction: Background
Compression saves
  Bandwidth
  Storage space
  Transmission time
  BETTER SYSTEM EFFICIENCY!
Compression in Communication System Architecture
Global Communication System [3]

## Slide 5: 1. Introduction: Background
The modern data compression is based on Claude Shannon’s paper “A Mathematical Theory of Communication” published in 1948. [1]
Application of data compression is ENORMOUS!!
Used in both software and hardware devices.
Huffman | Lempel-Ziv
JPEG | GIF
FAX MACHINES | ZIP
MP3 | UNIX File system
Claude Elwood Shannon (1916–2001) [4]
Applications of compression codes [5]

## Slide 6: 1. Introduction: Motivation & Challenges
Challenges
  Compression efficiency should be 3:1 or 2:1.
  Efficient implementation
  UNIVERSAL:
  The code responds to different inputs.
  Error free decompression
Motivation:
  Implementations of compression algorithms on information source with/without memory
Challenges of compression codes [5]

## Slide 7: 1. Introduction: Project Description
Huffman compression Encoder
Huffman compression Decoder
Adaptive Huffman Codebook
Adaptive Huffman Decoder
Adaptive Huffman Encoder
Main Objective: Implement, evaluate and stress-test selected Data compression techniques.
Identified the following algorithms for designing:

## Slide 8: 2. Huffman Compression Algorithm

## Slide 9: 2. Huffman Compression Algorithm
Macmillan Inequality
Shannon Compression Theorem
Equation
Must be satisfied by any Uniquely Decodable code
Huffman Algorithm always satisfies it. [5]
Equation
Set the limits for the maximum compression of any code [5]

## Slide 10: 2. Fixed Huffman Code Example
X | P(x)
A | 0.5
B | 0.3
C | 0.2
A
B
C
0.5
0.3
0.2
0.5
0
1
0
1
1.0
Merge least two probabilities
Assign ‘0’ to higher probability and ‘1’ to lower probability
Repeat
A -> 0
B -> 10
C -> 11
Traverse on the Huffman tree to form the codebook
Mcmillian: 1
E(l) = 1.5
H(x) = 1.49
H(x) + 1 = 2.49

## Slide 11: 2. Universal Huffman Algorithm Implementation

## Slide 12: Module 1: Combine Probabilities function
P = [0.4, 0.3, 0.3]
i = 1
0.6 > 0.4 ?
q = [0.6, 0.4]
CB_split = []
CB_split = [1]
P = [0.6, 0.4]

## Slide 13: Module 2: Generate Codebook function
CB_split = [1]
CB = [0, 1]
L = [1, 1]
split = 1
L = [2, 1]
L = [2, 2, 1]
L = [1, 2, 2]
CB = [00, 10]
CB = [00, 00, 10]
CB = [00, 01, 10]
CB = [10, 00, 01]

## Slide 14: Module 3: Universal Encoder
00
‘a’
‘b’
‘c’
1
01
Source_Index = 1;
Length source = 3;
Source = ‘bca’
Source_Index = 2;
Length source = 3;
Source_Index = 3;
Length source = 3;
Comp_String = 00
Comp_String = 0001
Comp_String = 00011
Source_Index = 4;
Length source = 3;
Compr_String = 00011

## Slide 15: Module 4: Universal Decoder
00
‘a’
‘b’
‘c’
1
01
Codebook:
Comp_String = 00011
n = 1
n = 2
dataHAT = b
dataHAT = bca

## Slide 17: 2. Huffman Algorithm: Implementation Constraints
Initial encoder/ decoder structure
  Used hard- coded codebook of fixed source
  Tests with varying data lengths and randomly generated data
Efficiency test
  Tests with varying data of fixed size
  Tested encoder’s efficiency
Universal Codebook generator
  Tried binary tree data structure 
  Used built in sorting functions 
  Codebook has varying lengths. Cannot be stored as matrix 
  Implemented manual sorting 
  Developed L vector to track code-word length 
Universal encoder/ decoder
  Used universal codebook generator in encoder/ decoder
  Implemented test bed to test overall algorithm
A
B
C
0.5
0.3
0.2
0.5
0
1
0
1
1.0
KEY CHALLENGE: LEAVES TO ROOT in Huffman tree construction use RECURSIVE implementation

## Slide 18: 2. Huffman Algorithm: Efficiency
Example:
  ‘0’ -> 1 – p = 0.5
  ‘1’ -> 00 - p = 0.3
  ‘2’ -> 01 - p = 0.2
Efficiency?
  E(l) = ∑ pi × li
  in bits/symbol
Efficiency = 0.5 × 1 + 0.3 × 2 + 0.2 × 2 = 1.5 bits/symbol
Test: Observe what happens when compression is performed 1000 times for random data of fixed lengths.
Length of data is 5, 25 and 100 symbols for figures (a), (b) and (c) respectively in the next slide.

## Slide 19: 2. Huffman Algorithm: Observations of efficiency test
Efficiency of compressed data follows a normal distribution
Most of the data compressed is close to the efficiency of 1.5 bits/source symbol
The distribution is narrower for larger data size
Fig a: Data size = 5
Fig b: Data size = 25
Fig c: Data size = 100

## Slide 20: 3. Conclusion
Learnt and implemented UNIVERSAL Huffman compression
Learnt design and implementation of signal processing functions in MATLAB
Used important performance evaluation techniques, such as the histograms for efficiency
Started research on other important algorithms required for the next part of the project; Lempel-Ziv and the turbo compression.
Some possible applications:
  Hard Coded Huffman: Could be used in the Twitter data base to compress tweets which have the same content
  Adaptive Huffman: Image in JPEG format, compression of hyperspectral data from satellites

## Slide 21: 4. Work Breakdown and Future Work
Semester’s Timeline
April

## Slide 22: 4. Work Breakdown and Future Work
New
Functions
Lempel-Ziv
Run-length Coding
Merge the new code with the old
Create a source generation file
Use histograms for efficiency testing
Testing On
Data Sources
Merge the functions and implement on actual data sources. For example: images, folders
Turbo Compression
Plan For Next Semester

## Slide 23
4. Work Breakdown and Future Work
Plan For Next Semester

## Slide 24: 5. References
[1] S. W. 2002, "Historical notes: History [of data compression]," 2002. [Online]. Available: https://www.wolframscience.com/reference/notes/1069b.
[2] R. T. Snodgrass, Radio Receiving for Beginners, V. F. Camp, Ed. New York: The MacMillan Company, 1992.
[3] A-Read, "Satellite communication systems," in A Read. [Online]. Available: http://www.a-read.com/satellite-communication-systems/.
[4] Bell Labs, "Claude Elwood Shannon 1916-2001," in wikipedia.com, 2011. [Online]. Available: http://it-science.net/images/shannon.small.jpg.
[5] J. G. Proakis, Communication Systems Engineering, M. Salehi, Ed., 2nd ed. Pearson, 2001.
Thank You!

## Slide 25: Backup Slides

## Slide 26: Software Used
Used MATLAB to code these functions.
Reason for choosing MATLAB:
  It’s extensive Math Library.
  Easy to deal with vectors and matrices
Implementation on other programming languages, for example C or JAVA, will be very simple after coding on MATLAB.

## Slide 27: Source Encoder/Decoder

## Slide 28: Channel Encoder/Decoder

## Slide 29: Universal Communication Systems Architecture

## Slide 30: Huffman Encoding: Practical Example

## Slide 31: Semester’s Timeline